## Slide 1: Helicopter Vibration and RTB
Jim Fackler, Helicoptger Technology Company
5 MAR 2019
Atlanta GA

## Slide 2: Overview
Machines and Vibration Overview
What is vibration?
  Displacement
    Mils (.001 inch) peak to peak
  G
    Change in direction
  Velocity
    Speed through zero crossing
  Phase
    When it happens in a cycle

## Slide 3: Vibration Basic
Vibration is the oscillation of an object having a forcing function.
The oscillation may be periodic or random
  Out of balance is periodic
  Most aerodynamic functions are periodic
  White noise (ex continuous combustion) is random

## Slide 4: Vibration Basic

## Slide 5: Vibration Basic – The sine wave

## Slide 6: High Frequency Vibration

## Slide 7: Vibration Basic
Vibration is the oscillation of an object having a forcing function.
The oscillation may be periodic or random
  Out of balance is periodic
  Most aerodynamic functions are periodic
  White noise (ex continuous combustion) is random

## Slide 8: Vibration Basic
Vibration is the oscillation of an object having a forcing function.
The oscillation may be periodic or random
  Out of balance is periodic
  Most aerodynamic functions are periodic
  White noise (ex continuous combustion) is random

## Slide 9: Basic Aerodynamics
The forces acting on a helicopter blades are the same as those acting on an airplane wing, but with different consequences

## Slide 10: Blade Dynamics
FLAP
PITCH
LEAD / LAG

## Slide 11: BLADE TRACK
TIP PATH
VERTICAL FORCES

## Slide 12: STROBEX TRACK
TIMED FLASH FROM TRIGGER ON SWASHPLATE

## Slide 13: STROBEX TIP TARGET

## Slide 14: OPTICAL TRACKER
PASSIVE OBSERVATION OF BLADE SHADOW THROUGH A ‘GATE’

## Slide 15: OPTICAL TRACK PRESENTATION

## Slide 16: PROS /CONS OF TRACK AND TRACK DEVICES
TRACKING FLAG
PROS
Inexpensive. Easy to interpret
CONS
Can only be used on ground. Hazardous in gusty winds.
Require two crew members
Unlikely to resolve track to a smooth ride

## Slide 17: PROS /CONS OF TRACK AND TRACK DEVICES
STROBEX
PROS
“Live” unprocessed image. Easy to interpret. Can be used in any flight or ground mode. May be used independently of processor.
CONS
Track “targets” may affect blade flight. Target material may erode in rain.
Does not input to processor for archive or solution generation.
Chance a good track does not result in a good ride.
Difficult to see in some lighting conditions

## Slide 18: PROS /CONS OF TRACK AND TRACK DEVICES
OPTICAL TRACKER
PROS
Accurate when working properly. Passive – no need to attach targets. Can be archived. Very good at diagnosing lead / lag problems
CONS
Subject to optical errors. Processed image may not show transient events.
If track data is in error and the solutions are generated based on optical track image, success in track and balance is doubtful.
Handheld ones are subject to errors due to aircraft motion.
Good tip path ay not be best ride.

## Slide 19: VERTICAL VIBRATION SENSOR

## Slide 20: VERTICAL VIBRATION SENSOR
Always gives correct information on vertical ride quality.
Visual track is correct only 90 % of the time

## Slide 21: VERTICAL VIBRATION SENSOR
Must be used with a polar chart or solution generating balancer
Readings may be corrupted by Lateral imbalance or worn components

## Slide 22: Vertical Polar Chart
Polar charts are flight condition specific
Solutions may be tab or pitch change rod

## Slide 23: PITCH CHANGE ROD
Entire blade angle is increased increasing lift or decreased decreasing lift.
REMEMBER! Any time lift is increased, drag is also increased

## Slide 24: TRIM TAB
Increasing affect as airspeed increases
Changes collective forces

## Slide 25: TRIM TAB – How it works
Up tab causes a down force on the trailing edge causes the blade to pitch up. This is OPPOSITE the way it works on a Fixed Wing!

## Slide 26: TAB TOOLS
Most tabs are measured in degrees
Newer designed tools measure tab displacement in Mils
Beware! Some Eurocopter tools measure up tab in MINUS degrees opposite to industry standards

## Slide 27: LATERAL VIBRATION
Due primarily to imbalance in the rotor plane of rotation

## Slide 28: SYNCRONIZING EVENTS
Typically a magnetic pickup is triggered by a ferrous interrupter
Must be ferrous
Requires a close proximity
.050” Typical

## Slide 29: MAGNETIC PICKUP
Syncronizes Strobex
Syncronizes blade order for optical trackers
Provides a reference point from which phase angle is derived
Sets band pass filtering for accelerometers

## Slide 30: MAGNETIC PICKUP
Magnetic pickup identifies master blade from which adjustments are referenced
Screw this up and you are in for a long day

## Slide 31: Photocell as a one per rev trigger

## Slide 32: Photocell
Triggers off reflective tape
Require “dwell”
Time.

## Slide 33: MAIN ROTOR SMOOTHING SEQUENCE
For articulated rotors…
  Ground track
  Hover track
  Inflight track
  Balance
  Check and adjust autorotation

## Slide 34: MAIN ROTOR SMOOTHING SEQUENCE
For semi rigid rotors…
  Ground track
  Hover track
  Hover balance
  In flight track
  Check and adjust autorotation

## Slide 35: Main rotor strategies
Go for broke with all adjustments
  Good for minor touch up
  Disastrous for new blades
  Familiarity with rotor essential
  OK with later smart chart algorithms that have proven track record

## Slide 36: Main rotor strategies
Sequential adjustments
  Best bet for new blades
  Slower than go for broke (maybe)
  Easier to diagnose rotor problems
  Can be used with smart technologies

## Slide 37: Helpful hints
Record all readings and adjustments
  Try to replicate readings on adjustment removal
  Verify correct direction checking against track picture
  Have same mechanic make the changes
  Do not deviate from airspeeds or flight conditions when taking reading results.

## Slide 38: Processors and Analyzers
Q: Why aren’t we talking about the instruments that process the signals?
A: User and use preference

## Slide 39: Processors
Salient points
Cheaper balancers put more burden on user experience and qualification. They are more generic and not bound to specific software.
Expensive Balancer / Processors are typically more capable and lend themselves to data archiving and data bases. Tied to aircraft specific software.
BOTH CAN DO A FINE JOB OF EOTOR SMOOTHING

## Slide 40: TAIL ROTOR
Generally treated s a single plane balance
More susceptible to sympathetic resonance making balance difficult

## Slide 41: TAIL ROTOR
Small weight changes can have a large effect!
Weigh weight accurately
Feather bearings and trunnion preload are biggest problem.

## Slide 42: SPECTRUM ANALYSIS
Vibration spectra consist of frequency on the X axis (increasing left to right), and amplitude (amount) on the Y axis – bottom to top.

## Slide 43: Frequency Identifies Component
Main Rotor 487 @ 100%
Eng N1 50790
Eng N2 33,000
Eng Output 6000
TR DS 2120
TR 2900
TR 2 rev 5800
Main bevel Gear mesh ~22000
PTO Gear mesh 301000
TR gear mesh 65000

## Slide 44: Tying it together

## Slide 45: Spectrum Analysis
Think in terms of Cycles per minute instead of RPM
Gear box gear mesh rates can be very high

## Slide 46: How to use Spectrum to your advantage
One time shot
  If you know exceedance amplitude numbers you know exactly what to look at to correct
  Digital media can be shared among other technical staff
  Largest peaks are generally what you feel
  Try to standardize on locations
  Can be compared to other aircraft

## Slide 47: How to use Spectrum to your advantage
Sequence of data over time
  It is always best to judge an aircraft against itself
  Trends can be monitored over the aircrafts history
  Interval has to be short enough to catch incipient problems
  Interval has to be long enough to allow helicopter to change

## Slide 48: How to use Spectrum to your advantage
Health and Usage monitoring
  Can provide real time monitoring
  Requires a substantial investment in equipment (per aircraft) and personnel (someone has to look at and judge serviceability)
  Cost effective for large aircraft or where down time needs to be minimized

## Slide 49: Q & A
This presentation has been brought to you compliments of Helicopter Technology Company, Los Angeles, California
See us at Booth C4302